## Slide 1
Analysis and synthesis of analog filters

## Slide 2
System concepts:
A system is a process that produces a signal at its output (or reaction), noted for example y(t), when it is excited at its input by a signal (or action) that we note for example x(t).
It is then said that y(t) is the effect of the system on x(t).
One can model (represent mathematically) a system by an equation linking the input x(t) to the output y(t).
GENERAL
System
Input x(t):
signal or action
Output y(t):
signal or reaction
x(t)
y(t)
fct: refers to a mathematical function

## Slide 3
Analog system
SISO
Analog system
MISO
Analog
System
SIMO
Analog
System
MIMO
x(t)
y(t)
y(t)
x(t)
y1(t)
yM(t)
y1(t)
yM(t)
x1(t)
xN(t)
x1(t)
xN(t)
A system may produce one or more signals at its output, as it may be excited at its input by one or more other signals
Single Input Single Output
Multiple Inputs Single Output
Single Input Multiple Outputs
Multiple Inputs Multiple Outputs
GENERAL

## Slide 4
A system can therefore be:
electric: Electrical circuit, electric motor
electronics: sensor, amplifier, filter
automatic: regulator
telecommunication: a modulator, a demodulator, transmission channel ... etc
mechanical: spring, pendulum, mechanical motor
political
economic
.... etc
Obviously, each type of system has its own input and output signals (or parameters)
GENERAL

## Slide 5
Resistance R: with v the voltage at its terminals and i the current that flows through it
Inductance L: with v the voltage at its bornes eti the current that runs through it
Capacitor C: with v the voltage at its terminals and i the current that flows through it
R
i
GENERAL
Examples of systems: We will focus more particularly on electrical systems. The first three are linear and the last non-linear.
v
i
L
i
C
v
v
Diode D: v the voltage at its terminals and i the current that passes through it

## Slide 6
GENERAL
Examples of systems: Among the most frequently used electrical systems are linear and time-invariant systems (SLIT).
As we can notice on this simple and basic example, the mathematical relation that links the input x(t) to the output y(t) is in the form of a first-order differential equation:
differential equation systems always represent linear systems.
Moreover, constant coefficients indicate invariance over time.

## Slide 7
noises
transmitter
RECEPTOR
GENERAL
Examples of systems: transmission chains
A communication system (Transmitter, Channel and Receiver) is formed by a set of systems. The source, encoders, modulator, channel, demodulator, decoders are examples of often complex systems.

## Slide 8
    Ressort : raideur = k
    Amortisseur : coefficient de frottement = b
Weight is taken into account in the operating point (f0 = mg, y0)
m
f
k
b
y
y0
GENERAL
Examples of systems: Mechanical system

## Slide 9
The system is linear if:
For the input we have the output
For the input we have the output
For an entry we have
Where and are real constants
. Linear system:
DEFINITION OF A SLIT
Analog system
Input x(t) :
Output y(t) :
x(t)
y(t)

## Slide 10
From a mathematical point of view: A linear system is one in which the relations between input and output quantities can be expressed as a set of differential equations with constant coefficients
Where the coefficients ak et bl are real constants
Generally N≥M. We then say that the system is of order N
DEFINITION OF A SLIT
1. Linear sustem:

## Slide 11
2 . Time-invariant system:
A system is invariant when the behavioral characteristics do not change over time. In other words, a system is invariant when its response (its output) does not depend on the moment when the input signal is applied.
For the input an invariant system gives
So for an input it must give
Example 1: Invariant system Example 2: invariant system
DEFINITION OF A SLIT

## Slide 12
4. Impulse response of an SLIT:
The impulse response of an SLIT, often denoted as h(t), is the output of the system when its input is a Dirac pulse.
For then
For then
For
The output
Taking into account both the linearity and invariance of the system
3. Causal system:
A system is causal if for any causal input the output must be causal
DEFINITION OF A SLIT
:

## Slide 13
THE CONVOLUTION FOR A SLIT
Taking into account their linearity and invariance properties, we can then use the convolution equation to describe SLIT in the time domain
SLIT analogique
Entrée x(t) :
x(t)
y(t)
Time domain
Frequency domain
TF
TF-1

## Slide 14
THE CONVOLUTION FOR A SLIT
SLIT analogique
Entrée x(t) :
x(t)
y(t)
To better understand this convolution equation and how it is calculated, let’s take another example of an analog signal x(t) applied to the input of a SLIT. It can be considered as an infinity of Dirac impulses (see figure below.
Taking into account the invariance property, each pulse of this signal will create at the output of the SLIT an offset impulse response and with the amplitude of the pulse (or the signal at the time of the pulse).
Taking into account the linearity property, the global output y(t) will therefore be the sum of all contributions due to each pulse of the input signal

## Slide 15
THE CONVOLUTION FOR A SLIT
So, assuming that the thus considered pulses of the input signal are spaced from each other by delta , we will have:

## Slide 16
DIFFERENTIAL EQUATIONS FOR A SLIT
An SLIT can also be represented in the time domain by differential equations always between input x(t) and output y(t), of the form:
coefficients ak et bl are constants,
NM : order of SLIT

## Slide 17
The transformation of Laplace H(p) = TL(h(t)) is the function of the complex variable p defined by:
  p :operator of Laplace, noted also s
THE TRANSFORMATION OF LAPLACE
The analysis of SLIT (analog filters) is usually carried out using the Laplace transform.
The Laplace transform is also called the generalized Fourier transform. Indeed, it can converge where the Fourier transform can diverge.

## Slide 18
Linearity :
Delay or translation :
Modulation:
Derivation :
Integration:
Initial value:
Final value :
PROPERTIES OF THE LAPLACE TRANSFOFRMATION

## Slide 19
As we have already explained above, the Laplace transform is considered a generalized Fourier transform. In other words, the Fourier transform is a special case of the Laplace transform
PS: The terminals of the integral are from 0 to + +∞ because we assume that h(t) is causal (h(t)=0 for t<0
RELATIONS BETWEEN TL AND TF
Laplace Transform
Fourier Transform

## Slide 20
We assume the cond. init. nulls; the application of the TL leads to:
where the transfer function H(p):
The transfer function H(p) is therefore a ratio of a numerator N(p) (p-order polynomial M) to a denominator D(p) (p-order polynomial N)
SLIT TRANSFER FUNCTION

## Slide 21
In H(p), we can factor a0 and b0:
  K represents the static gain
  Htrans(p) represents the transient regime
  The order of the SLIT is set by N≥M
SLIT TRANSFER FUNCTION

## Slide 22
The frequency response H(f) of an SLIT is a special case of the transfer function H(p),
In fact for
The gain in dB of an SLIT can be represented by:
The phase shift brought by the SLIT on the output signal compared to the input signal is given by:
FREQUENCY RESPONSE OF A SLIT

## Slide 23
The bandwidth (BW) of an SLIT is the frequency range limited by the cut-off frequency(ies). The cut-off frequencies correspond:
They also correspond
We often talk about cut frequencies at -3dB
FREQUENCY RESPONSE OF A SLIT

## Slide 24
STABILITY OF SLIT
An SLIT is known to have a transfer function H(p) that is formed by a ratio of two polynomials in p.
Therefore, we can calculate the roots of N(p) and also the roots of D(p).
The roots of N(p), where particular values of p cancelling the numerator, are called the zeroes of H(p)
The roots of D(p), where particular values of p canceling the denominator, are called the poles of H(p)
where zl=l+jl= l+j2fl are zeroes of H(p) assuming they are simple roots
Where are poles of H(p) assuming they are simple roots

## Slide 25
Zeroes of H(p) are zl=l+jl= l+j2fl
Poles of H(p) are
We can therefore represent in the plane p (reference where the axis of the amplitudes is j the imaginary part of p and the x-axis is  the real part of p.
The zeroes are represented by °
The poles are represented by x

j
X
X
X
X
0
0
0
Plan p
Example of a plan p of an SLIT of order 4
In this example, we have four poles all with a negative real part and three zeros, one of which has no imaginary part.
STABILITY OF SLIT

## Slide 26
An SLIT is stable if for any input x(t) bounded in amplitude its output y(t) is also bounded in amplitude. In other words, a stable SLIT is a Bounded Input Bounded Output (BIBO) system.
SLIT stable
x(t)
y(t)
Stability condition in the time domain
In the spectral domain, from the p plane, an SLIT is stable if all its poles are in the left half plane of the p plane. That is to say, all its poles have a real negative part ()
Therefore, it is enough that a single pole of H(p) lies on the imaginary axis of the plane p (its null real part) or in the right half-plane (its positive real part) for this system to become unstable..
STABILITY OF SLIT

## Slide 27
SLIT EXAMPLES: ANALOG FILTERS
Among the most requested analog SLIT, we have analog filters. The study and analysis of these analog filters, like all SLIT, is carried out in the time domain but also and especially in the frequency domain. In the spectral domain we need:
of the transfer function in p, H(p) which allows us among other things to:
know the zeroes and poles of the filter
determine the eventual stability of the filter
know the static gain of the filter
...etc
of the frequency response H(f), a particular case of H(p), which allows us among other things to know :
the filter template (gabarit du filter)
its response in amplitude
its response in phase
the type of the filter

## Slide 28
SLIT EXAMPLES: ANALOG FILTERS
There are four types of depth (fondamentaux) analog filters:
Low-pass filter: Its BP bandwidth is limited between 0 Hz and a high notched cutoff frequency fc
High-pass filter: Its BP bandwidth is limited between a notched cutoff frequency fc and a very high-frequency cutoff frequency (theoretically, the latter tends towards infinity)
Band-pass filter: Its BP bandwidth is limited between a rated low cutoff frequency fcb and a rated high cutoff frequency fch
Notch filter (reviewer): Its passbands BPb and BPh are limited respectively
- between 0 Hz and a low cutoff frequency noted fcb for BPb
- between a high cutoff frequency rated low fch and a very high-frequency cutoff frequency (theoretically the latter tends towards infinity) for BPh

## Slide 29
The Low-Pass filters (only let low frequencies pass)
f
H(f)
0
fc
BP
Frequency response of an ideal low-pass filter
f
H(f)
0
BP
fc
Frequency response of a real low-pass filter
SLIT EXAMPLES: ANALOG FILTERS

## Slide 30
Les filtres Passe-Haut ( ne laissent passer que les fréquences hautes )
f
H(f)
0
fc
BP
Réponse fréquentielle d’un filtre passe-haut idéal
H(f)
0
BP
fc
f
Réponse fréquentielle d’un filtre passe-haut réel

## Slide 31
Band-Pass filters (only allow a range of frequencies to pass)
f
H(f)
0
fcmin
BP
Frequency response of an ideal bandpass filter
fcmax
f
0
fcmin
BP
fcmax
Frequency response of a real band-pass filter
H(f)
SLIT EXAMPLES: ANALOG FILTERS

## Slide 32
The Notch filters (do not let a frequency range pass). Also called rejection filter
f
H(f)
0
fc1
BP1
Frequency response of an ideal notch filter
fc2
BP2
f
0
fc1
BP1
fc2
BP2
Frequency response of a real notch filter
H(f)
EXEMPLES DE SLIT : FILTRES ANALOGIQUES

## Slide 33
SYNTHESIS OF ANALOG FILTERS
The synthesis of an analog filter involves determining:
  the usual form to adopt,
  Filters from Butterworth
  Chebychev filters I and II
  Cauer or Elliptical Filters
the spectral characteristics as close as possible to what is desired, in particular the filter template and the order of the filter
its response in phase and its group time
The structure of the filter (if it is active) to be carried out
  Rauch’s structure
  Sallien-Key structure
  This will allow us to obtain the values of passive electronic components (R, L and C or even based on piezoelectric components) and active (semiconductor components such as transistors and operational amplifiers). necessary for the implementation of the analog filter

## Slide 34
SYNTHESIS OF ANALOG FILTERS
Below are the essential steps to follow when synthesizing an analog filter:
Specifications of the analog filter to be made: TEMPLATE
Normalized Template: Determination of the Filter Order
Type of usual filters to be used (Butterworth, Chebychev ) in normalized form (Low-pass with cutoff pulsation c = 1)
Step of denormalization: Filter to be carried out of any type (low-pass, high-pass ...etc) and pulsation of any cut.
Choice of the structure to be used for the design (Rauch, Sallien-Key, Biquadratic ....etc)

## Slide 35
ANALOG FILTER TEMPLATES
Below is an example of a template for an analog low-pass filter that one wishes to create. These are simply the main tolerated characteristics of the Gain (module of the frequency response) of the filter to be achieved, namely:
the bandwidth: here between 0 and f1
The transition band width between f1 and f2
The undulations tolerated in the BP that one notes 1
The undulations tolerated in the cut or blocked band that one notes 2

## Slide 36
ANALOG FILTER TEMPLATES
0 f1 f2 f
2
1+1
1-1
Below, an example of a frequency response of a low-pass filter that conforms well to the imposed template
Generally, ripple rates(taux d’ondulation) within the bandwidth (Rp) and in the cut band (Rs) are determined in dB, using the following formulas:

## Slide 37
ANALOG FILTER TEMPLATES
We can easily deduce the shape of the templates from other types of filters, namely: high-pass, band-pass and notch.

## Slide 38
ANALOG FILTER TEMPLATES
Generally, the transfer functions of the mostly usual analog filters are standardized (cutoff pulse c = 1) and represent low-passes. When one wishes to create another type of filter with any cut-off pulsation, one must denormalize.
Normalized usual low pass: Put
Denormalization of a usual low-pass: Replace
Denormalization of a usual high pass: Replace
Denormalization of a usual bandpass: Replace
Denormalization of a usual band-stop: Replace

## Slide 39
THE USUAL ANALOG FILTERS
Butterworth Filter
Among the usual analog filters, the Butterworth filter is the one that has the most constant gain possible in the passband and tends towards 0 in the cutoff band.
However, it has one of the widest transition bands.
H(f): Frequency response of a low-pass Butterworth filter
fc: filter cutoff frequency
N: Filter order
H(p): Low-pass Butterworth p transfer function
c : filter cut-off pulsation
N : filter order

## Slide 40
THE USUAL ANALOG FILTERS
Filtres de Chebychev I
It guarantees a better selectivity (low transition band) at the expense of a presence of ripples in the bandwidth. The maximum value of these ripples is a design parameter of the filter.
Is determined by the following recurrence:
H(f): Frequency response of a low pass Chebychev I filter
fp: defining the bandwidth
 :Ripple rate in the bandwidth,
N: Filter order

## Slide 41
THE USUAL ANALOG FILTERS
Chebychev II filter
It also guarantees good selectivity (low transition band) at the expense of a presence of undulations this time in the cut band
H(f): Frequency response of a low pass Chebychev filter I
fs: delimiting the cut band
 :Ripple rate in the bandwidth,
N: Filter order
Is determined by the following recurrence:

## Slide 42
THE USUAL ANALOG FILTERS
Elliptical Filters (from Cauer)
They also ensure good selectivity (low transition band) at the expense of a presence of undulations this time in the bandwidth and in the cut-off band.
Cauer or elliptical filters have three degrees of freedom, unlike other filters which have only two at most: their order, the bandpass undulation and the stiffness of the cut-off, which also determines the minimum attenuation in the stop band.
H(f): Frequency response of a low pass Chebychev filter I
fp: defining the bandwidth
fs: delimiting the cut band
 :Ripple rate in the bandwidth,
N: Filter order
: Chebychev’s rational function
Unlike the Butterworth and Chebychev filters, which are all-pole filters, Cauer or elliptical filters have zeroes and poles.

## Slide 43
THE USUAL ANALOG FILTERS
comparison
Source : Wikipédia
Below are the frequency responses of the four types of usual analog filters